## Slide 1: Canary SRAM Built in Self Test for SRAM VMIN Tracking
ECE 7502 Class Proposal
Arijit Banerjee
12th Feb 2015

## Slide 2
Requirements
Specification
Architecture
Logic / Circuits
Physical Design
Fabrication
Manufacturing Test
Packaging Test
PCB Test
System Test
PCB Architecture
PCB Circuits
PCB Physical Design
PCB Fabrication
Design and Test Development
Customer
Validate
Verify
Verify
Test
Test

## Slide 3: Motivation
Deep submicron high density SRAM: write worsen
  Requires assist in deep submicron technology [Zimmer et al 2012]
    constant energy and area overhead
  Techniques like dual rail is expensive alternative to assist
SRAM dynamic write minimum operating voltage (VMIN )not constant
  Need to track SRAM write VMIN across PVTs
  Need to turn on or off assists when required and save energy
Canary SRAM to the rescue
  Closed loop dynamic VMIN tracking
  Requires built in self test (BIST) for continuous operation

## Slide 4: Canary SRAM
An SRAM sensor that can be sensitive to retention, read, write
  Uses a reverse assist to degrade operations
Canary data retention voltage (DRV) tracking [Wang et al 2007]
Canary write VMIN tracking [Banerjee et al 2014]
  Uses BIST to count the # of bit failures
  User knobs: failure threshold and degree of reverse assist

## Slide 5: Outline
SRAM faults and state of the art for SRAM BIST algorithms
Canary BIST challenges
Approach: proposed canary BIST
Important metrics and expected outcomes
Deliverables and timeline

## Slide 6: SRAM Faults and State of The Art for SRAM BIST algorithms
SRAM Faults
  Static
    Stuck at faults (SAF)
    Address decode faults (AF)
    Transition faults (TF) etc.
  Dynamic
    Recovery faults
    Retention faults etc.
March algorithms
  MATS, MARCH X, MARCH C- etc.
Memory BIST Trends
  Programmable BIST [Zarrineh et al 1999][Kokrady et al 2008] [Fradi et al 2011]
  Processor controlled BIST [ Ching-Hong Tsai et al 2001]

## Slide 7: Canary BIST challenges
Canary BIST requirements
  Manufacturing test for canary SRAM and BIST itself
  At speed test for supporting user requirements in an system on chip (SoC)
Challenges
  At speed continuous testing for canary failures during manufacturing and user run conditions
  Compute failure rate within a few cycles
  Alert the user for assist related changes
  Power challenges
  Canary BIST testing itself

## Slide 8: Approach: Proposed Canary BIST
Focus
  Go/No-Go memory mode BIST for manufacturing test
  Failure rate compute in canary BIST mode
  To cover only the SAF, AF and TFs of canary SRAM using canary BIST
Algorithm Implementation in canary BIST
  MARCH X or MARCH C- in RTL
Low power Implementation
  RTL with clock gating support
  Power gating support
Compute incremental canary failure rate
  After every write followed by read in the same address
  User defined cycles
    Tight write and relaxed read with options

## Slide 9: Important Metrics and Expected Outcomes
Fault coverage
  MARCH X or MARCH C- : guarantees 100% fault coverage (SAF, AF and TFs only)
  Fault coverage of the canary BIST itself: 99% target coverage using DFT scan chains
Test access time
  Time to do a Go/No-Go test for 512 bit canary
Data volume
  Amount of tester data required to test
    Canary SRAM
    Canary BIST
Expected results
  March test RTL simulations for implementation
  SPICE results for CBIST Go/No-Go test after synthesis
  SPICE results of test access time after synthesis
  Fault coverage result for the canary BIST itself using Synopsys TetraMAX

## Slide 10: Deliverables and Timeline
Deliverables | Expected Date | Actual Date | Status | Issues
RTL for March Test and Verilog simulation results | 2/24/2015 |  | Planned | 
Synthesis using DC with IBM 130nm | 2/28/2015 |  | Planned to report on 3/3/2015 | 
SPICE Simulation results Go/N-Go and test access time | 3/14/2015 |  | Planned | 
Canary BIST Fault coverage results | 3/21/2015 |  | Planned to report on 3/24/2015 | 

## Slide 11: References
[1] J. Wang and B. Calhoun, “Canary replica feedback for near-DRV standby vdd scaling in a 90 nm SRAM,” in Proc. Custom Integrated Circuit Conf. (CICC ’07), Sep. 2007, pp. 29–32.
[2] Banerjee, A.; Sinangil, M.E.; Poulton, J.; Gray, C.T.; Calhoun, B.H., "A reverse write assist circuit for SRAM dynamic write VMIN tracking using canary SRAMs," Quality Electronic Design (ISQED), 2014 15th International Symposium on , vol., no., pp.1,8, 3-5 March 2014
[3] B. Zimmer, S. O. Toh, H. Vo, Y. Lee, O. Thomas, K. Asanovic, and B. Nikolic, “SRAM assist techniques for operation in a wide voltage range in 28 nm CMOS,” IEEE Trans. Circuits Syst. II, vol. 59, no. 12, pp. 853– 857, Dec. 2012.
[4] Fradi, A.; Nicolaidis, M.; Anghel, L., "Memory BIST with address programmability," On-Line Testing Symposium (IOLTS), 2011 IEEE 17th International , vol., no., pp.79,85, 13-15 July 2011
[5] Zarrineh, K.; Upadhyaya, S.J., "Programmable memory BIST and a new synthesis framework," Fault-Tolerant Computing, 1999. Digest of Papers. Twenty-Ninth Annual International Symposium on , vol., no., pp.352,355, 15-18 June 1999
[6] Kokrady, A.; Ravikumar, C.P.; Chandrachoodan, N., "Layout-Aware and Programmable Memory BIST Synthesis for Nanoscale System-on-Chip Designs," Asian Test Symposium, 2008. ATS '08. 17th , vol., no., pp.351,356, 24-27 Nov. 2008
[7] Ching-Hong Tsai; Cheng-Wen Wu, "Processor-programmable memory BIST for bus-connected embedded memories," Design Automation Conference, 2001. Proceedings of the ASP-DAC 2001. Asia and South Pacific , vol., no., pp.325,330, 2001

## Slide 12
Questions and Feedbacks?